## Slide 1
Supervisor: Georgios Lampeas, Professor
Nikolaos Rigatos
Diploma’s Thesis Presentation
Investigation and numerical modelling of buckling and post-buckling behaviour of stiffened aircraft fuselage panels
Πάτρα, 13/07/2022

## Slide 2
Contents
Introduction
Purpose of study
Development of numerical models
Validation of numerical models
Numerical models of stiffened fuselage panels
Conclusions
Future work
References
2

## Slide 3
3
Introduction (1/2) – Stiffened panels
The fuselage is subjected to:
Axial tensile loads
Axial compressive loads
Combination of tensile/compressive loads
They are primarily constructed from:
Aluminum alloys
Multilayer carbon fiber–reinforced polymer (CFRP) composites
Stiffened Panel - Boeing 747-800 [1]
Skin
Frames
Stringers
3

## Slide 4
Introduction (2/2) - Buckling
4
Πάτρα, 13/07/2022
4
Buckling ● The loss of a structure’s ability to retain its configuration when subjected to external loads, leading to abrupt deformations and significant displacements.
α) Global buckling
β) Local buckling
[2]
Stable
Unstable
Neutral

## Slide 5
Purpose of study
5
Πάτρα, 13/07/2022
5
Investigation of numerical methods for predicting the buckling of stiffened shells
Parametrization of the problem
Validation of numerical models
Study of combined compression/shear buckling in stiffened fuselage panels
Validation of fuselage design
Main goals
1. Analytical equations
2. Experimental methods
3. FEM
Load cases:
Axial compression
In-plane shear
Combined compression/shear

## Slide 6
Development of numerical models
6
Method of Shared Nodes
SHELL181
6
  1. Geometry definition
  2. Element type definition
  3. Material characterization
  4. Meshing
  5. Boundary conditions
  6. Loads
  7. Buckling linear analysis solvers
  8. Solution
  9. Introduction of initial imperfections
  10. Boundary conditions
  11. Loads
  12. Buckling non-linear analysis solvers
  13. Solution
  14. Investigation of results
  15. Comparison and validation of results

## Slide 7
Validation of numerical models (1/9)
2
1. Axial compression load case
i. Plate
Ncr,FE | Ncr,an | ε
kN | kN | %
17.08 | 17.05 | 0.15
Qi [4]
Αριθμητικό μοντέλο
Timoshenko Analytical Equation [3]
7

## Slide 8
Validation of numerical models (2/9)
2
1. Axial compression load case
ii. Stiffened plate
8
Numerical model
Quinn et al[5]

## Slide 9
Validation of numerical models (3/9)
2
1. Περίπτωση φόρτισης αξονικής θλίψης
1. Axial compression load case
iii. Shell
9
1st eigenmode
2nd eigenmode
3rd eigenmode
4th eigenmode
The eigenmodes agree with Tran’s observations [6]

## Slide 10
Validation of numerical models (4/9)
2
1. Περίπτωση φόρτισης αξονικής θλίψης
1. Axial compression load case
iv. Stiffened panel
10
Numerical model
Wilckens et al[8]

## Slide 11
Validation of numerical models (5/9)
2
2. In-plane shear load case
i. Flat plate
σcr,FE | σcr,an | ε
MPa | MPa | %
9.83 | 9.74 | 0.86
11
Timoshenko analytical equation [3]
Numerical model
Amani et al [9]

## Slide 12
Validation of numerical models (6/9)
2
2. In-plane shear load case
ii. Stiffened plate
12
Αριθμητικό μοντέλο
Murphy et al [10]

## Slide 13
NACA design curves [11]
Επιβεβαίωση αριθμητικών μοντέλων (7/9)
2
2. In-plane shear load case
iii. Shell
σcr,FE | σcr,an | ε
MPa | MPa | %
100.1 | 103.3 | 3.16
13
σcr,FE | σcr,Domb [11] | ε
MPa | MPa | %
83.3 | 84.4 | 1.3

## Slide 14
Validation of numerical models (8/9)
2
2. In-plane shear load case
iv. Stiffened panel
14
Odermann and Kling [12]
Numerical model

## Slide 15
Validation of numerical models (9/9)
16
3. Περίπτωση σύνθετης φόρτισης θλίψης/διάτμησης
Buckling compression and shear interaction curve:
3. Combined compression/shear load case
i. Flat plate
15

## Slide 16
Numerical models of stiffened fuselage panels (1/3)
2
Material properties
Isotropic
Orthotropic
Aluminum Alloy
Ε 70GPa
ν 0.33
CFRP
Ε11 131GPa
E22 11.2GPa
ν12 0.33
G12 5.3GPa
G13 5.3GPa
G23 3.95GPa
Ply sequencing of orthotropic material
Shell
Stringers
[45,-45,0,90,-45,45,0]s
[45,0,-45,0,90]s
Geometry
Shell
Stringers
5 stringers
Distance of 150mm between them
Length of 600mm
800mm
750mm
2000mm
1.6mm
25mm
1.2mm
25mm
25mm
60°
16

## Slide 17
Numerical models of stiffened fuselage panels (2/3)
2
Element size | Ncr | ε
mm2 | kN | %
50x50 | 338.6 | -
25x25 | 238.7 | 41.8
12.5x12.5 | 220.7 | 8.17
10x10 | 218.7 | 0.90
5x5 | 217.5 | 0.56
Element size | Ncr | ε
mm2 | kN | %
50x50 | 408.9 | -
25x25 | 296.7 | 37.8
12.5x12.5 | 270.8 | 9.55
10x10 | 268.7 | 0.78
5x5 | 266.1 | 0.98
Numerical model and boundary conditions
Mesh convergence check
Aluminum
CFRP
Element size selected is 10x10mm2
17

## Slide 18
Numerical models of stiffened fuselage panels (3/3)
2
 | σcr,c [kN] | σcr,s [kN]
Aluminum | 416.3 | 229.1
CFRP | 322.7 | 142.4
ε (%) | 29 | 60
For the aluminum fuselage panel it is calculated:
For the CFRP fuselage panel it is calculated:
Results
18

## Slide 19
Conclusions
20
Αριθμητικά μοντέλα
The critical buckling load, the pre-buckling stiffness, the resulting mode shapes, and the failure mechanism are predicted with high accuracy.
The post-buckling behavior of the structures is computed with satisfactory accuracy.
The numerical models are fully parametric.
Σύνθετη φόρτιση ενισχυμένων κελυφών
In stiffened shells, the load interaction curve has the form:
Since northotropic < nisotropic, orthotropic stiffened shells are more sensitive to shear loads than their isotropic counterparts, highlighting the need for careful design of fuselage panels made from orthotropic materials compared to conventional aluminum panels.
Deviations in the post-buckling regime are due to:
Initial imperfections.
Plasticity models.
The modeling approach of the interface between the skin and stiffeners.
19

## Slide 20
Future work
2
Further development of numerical models
Validation of fuselage panel results
Validation for additional loading cases.
Incorporation of nonlinear phenomena for more accurate prediction in the post-buckling regime.
Parametric study of the effect of geometry, material properties, and ply orientation on the interaction curve.
Experimental investigation for the validation and enhancement of numerical model accuracy.
20

## Slide 21
References
2
[1] Terdiman Daniel, CNET, https://www.cnet.com/pictures/where-boeings-next-gen-747-8-comes-to-life-photos/34/
[2] N. Liu, “Global and local buckling analysis of stiffened and sandwich panel using mechanics of structure genome”, West Lafayette, Indiana, 2019
[3] S.P. Timoshenko, J.M. Gere, “Theory of elastic stability”, New York: McGraw-Hill, 1963
[4] L. Qi, “A study of the buckling behaviour of stiffened panels under compression and lateral Pressure”, 2018
[5] D. Quinn, A. Murphy, W. McEwan και F. Lemaitre, “Stiffened panel stability behaviour and performance gains with plat prismatic sub-stiffening”, Thin-Walled Structures, vol. 47, no.12, 1457-1468, 2009
[6] K. Tran και L. Davaine, “Stability of cylindrical steel panels under uniform axial compression”, Annual Stability Conference, Pittsburgh, 2011
[7] M. Domb και B. Leigh, “Refined design curves for compression buckling of curved panels using nonlinear finite element analysis”, 2011
[8] D. Wilckens, F. Odermann και Α. Kling, “Stringer stiffened panel under axial compression, shear and combined loading conditions – Test and numerical analysis”, European Conference of Composite Materials, Italy, 2012
[9] M. Amani, B. Edlund και M. Alinia, “Buckling and Postbuckling behaviour of unstiffened slender curved plates under uniform shear”, Thin-Walled Structures, vol. 49, 1018-1031, 2011
[10] A. Murphy, M. Price, C. Lynch και A. Gibson, “The computational post-buckling analysis of fuselage stiffened panels loaded in shear”, Thin-Walled Structures, vol. 42, 1455-1474, 2005
[11] M. M. Domb και B. R. Leigh, “Refined design curves for shear buckling of curved panels using nonlinear finite element analysis”, 43rd AIAA/ASME/ASCE/AHS/ASC Structures, Structural Dynamics, and Materials Con, Denver, Colorado, 2002
[12] F. Odermann και A. Kling, «Shear-Compression Buckling Test Method on Curved Stiffened Composite Panels,» σε European Conference on Composite Materials, Seville, Spain, 2014
21

## Slide 22
Thank you for your attention!
2